Spherical View Multi-Camera System Calibration
Andrey Filippov
Elphel, inc.
1405W. 2200S. #201
West Valley City

---
Calibration setup

---
Individual sensor front end (SFE) parameters (13)
6 extrinsic SFE parameters (relative to the target coordinate system):
X – lens axis on target plane X
Y – lens axis on target plane Y
L – distance from target along axis
φ– axis rotation around target Y
θ – axis elevation from XZ plane
ψ - camera roll around lens axis
7 intrinsic SFE parameters:
f – lens focal length
pX – pixel X of the lens axis
pY – pixel Y of the lens axis
a2..a5 - four radial distortion model polynomial coefficients

---
Sensor front end (SFE) location relative to the camera coordinate system
Camera has rotational symmetry around the vertical axis so cylindrical coordinates are convenient
h – SFE (lens center) height from the camera center
r –SFE distance from the camera vertical axis
azimuth – SFE angular position
φ– SFE optical axis rotation around the vertical camera axis from directly outwards
θ – SFE optical axis elevation from the plane perpendicular to the camera axis
Ψ – SFE roll angle

---
Parameters of the camera calibration machine
Camera position parameters (9):
     – constant (7) –
X – camera center X
Y – camera center Y
Z – camera center Z
φ-tilt – angle between the horizontal camera rotation axis and target X around target Y
Ψ – angle between the horizontal camera rotation axis and target X around target Z
inter-axis distance between rotational axes
inter-axis angle between rotational axes
    – variable (2) –
tilt – rotation around horizontal axis
axial – rotation around camera axis

---
Reprojection error remaining after
the radial distortion model

---
Image vignetting measured for green channel

---
Overlapping view areas of the 2 subcameras and frequency-domain linear features extraction

---
Multi-camera setups for controlled
depth of field video capturing